## Slide 1: Janus Optimizing Memory and Storage Support for Non-Volatile Memory Systems
Sihang Liu
Korakit Seemakhupt, Gennady Pekhimenko, Aasheesh Kolli, and Samira Khan

## Slide 2: SUMMARY
Problem and Motivation
The non-volatile memory (NVM) acts as both memory and storage
NVM systems require both memory and storage support
However, operations in memory and storage support increases write latency, which is on the critical path of NVM programs
Key Ideas
We observe that these operations can be divided into smaller sub-operations
We propose Janus, a software-hardware co-design that
  Parallelizes sub-operations if they are independent
  Pre-executes sub-operations if their dependencies are resolved
Performance
2X faster than serialized baseline

## Slide 3: BACKGROUND
The non-volatile memory (NVM) is
  High-speed
  Persistent
  Byte-addressable
NVM allows programs to directly manipulate persistent data in memory through a load/store interface
Different from conventional DRAM, NVM acts as both Memory and Storage
Intel 3D XPoint
A practical NVM system requires both memory and storage support
Notes: The new non-volatile memory is high-speed, persistent and byte-addressable. So it allows program to directly manipulate persistent data in memory though a load/store interface.
These features make non-volatile memory different from conventional DRAM – since it is both memory and storage
To make the integration of non-volatile memory practical, the system requires both memory and storage supports.

## Slide 4: MEMORY AND STORAGE SUPPORT
The memory and storage support is designed for
Security
Bandwidth
Endurance
Prevent attackers from stealing or tampering data
Encryption, integrity verification, etc.
Improve NVM’s limited bandwidth
Deduplication, compression, etc.
Extend NVM’s limited lifetime
Wear-leveling, error correction, etc.
We refer to the memory and storage support as
backend memory operations
Notes: These memory and storage supports are designed for different purposes, such as providing security guarantee, improving the bandwidth and extending the endurance.
We refer to the operations executed by these supports as backend memory operations.

## Slide 5: BACKEND MEMORY OPERATION LATENCY
Cache Writeback
Memory Controller
NVM Access
Write Access
Timeline
NVM
Core
Cache
Cache
Memory Controller
Cache
Memory Controller
Notes: Let’s take a look at its impact to the write latency.
In a system without these supports, the latency of a write consists of cache writeback, memory controller, and the NVM access.

## Slide 6: BACKEND MEMORY OPERATION LATENCY
Volatile
Non-volatile
Cache Writeback
Memory Controller
NVM Access
Backend Memory Operations
Write Access
Timeline
Recent NVM support guarantees writes accepted by memory controller is non-volatile
NVM
Core
Cache
Cache
Memory Controller
Cache
Notes: Recent non-volatile memory support (e.g., ADR) guarantee that writes accepted by the memory controller is persistent for better performance. As a result, only the cache writeback step is volatile.
However, when backend memory operations are integrated to the system, the latency between the write gets issued to the point it becomes persistent becomes much longer.

## Slide 7: BACKEND MEMORY OPERATION LATENCY
~15 ns
>100 ns
Latency to Persistence
Memory Controller
NVM Access
Backend Memory Operations
Cache Writeback
Write Access
Timeline
NVM
Core
Cache
Cache
Memory Controller
Volatile
Non-volatile
Notes: The latency is increased from around 15 ns to more than 100 ns if the system takes typical backend memory operations such as encryption, integrity verification and deduplication.
Add system stack on the left side

## Slide 8: WHY WRITE LATENCY IS IMPORTANT?
NVM
Core
Cache
Volatile
Non-volatile
persist_barrier
NVM programs need to use crash consistency mechanisms that enforces data writeback
Notes: Why the write latency is so important?
NVM programs need to ensure consistent recovery after failure using crash consistency mechanisms.
The figure shows an NVM system with volatile cache and non-volatile memory.
In order to guarantee data persistence, these mechanisms typically use persist_barrier to enforce the writeback.
So the execution is blocked by the writeback from cache to NVM.

## Slide 9: WRITE LATENCY IN NVM PROGRAMS
Example: Steps in undo logging transaction
persist_barrier
Writeback from cache
Timeline
Backup
Update
Commit
Execution cannot continue until writeback completes
Notes: Let’s take a look at the undo logging transaction that is commonly used in NVM programs to guarantee data’s crash consistency.
The transaction has three steps: backup the current data, perform the in-place update and finally commit the transaction.
Between each step, a persist_barrier is used to guarantee all updates have been written back to NVM before starting the next step. Execution cannot continue until writeback completes.
Reference to undo logging

## Slide 10: WRITE LATENCY IN NVM PROGRAMS
Write latency is on critical path
Timeline
Backup
Update
Commit
Crash consistency mechanism puts write latency on the critical path
Example: Steps in undo logging transaction
Notes: This way, the writeback from cache is on the critical path.

## Slide 11: WRITE LATENCY IN NVM PROGRAMS
Backend memory operations
Timeline
Backup
Update
Commit
Backup
Update
Commit
Increased latency
Backend memory operations increase the writeback latency
Notes: With the integration of backend memory operations, the latency of writeback becomes even longer.

## Slide 12
Backend memory operations are on the critical path
How to reduce the latency?

## Slide 13: OUTLINE
BACKGROUND AND MOTIVATION
KEY IDEAS
JANUS MECHANISM
EVALUATION
CONCLUSION

## Slide 14: OBSERVATION
Counter-mode
Encryption
Deduplication
Integrity
Verification
Each backend memory operation seems indivisible
Integration leads to serialized operations
Notes: These operations seem indivisible if we look at each of them. And, the integration of different operations results in a serialized latency.
This example shows encryption, integrity verification and deduplication need to happen one after another.
Explain why encryption is the last step

## Slide 15: OBSERVATION
However, it is possible to decompose them into sub-operations
Decompose
Generate counter
Encrypt counter
Data Encrypted counter
Counter-mode
Encryption
Generate MAC
(for integrity verification)
Notes: However, we observe that it is possible to decompose them into smaller sub-operations.
For example, the encryption operation, which is based on counter-mode, can be divided in to the following steps.

## Slide 16: KEY IDEA I: PARALLELIZATION
Deduplication
Integrity
Verification
Counter-mode Encryption
After decomposing the example operations:
Notes: To reduce the backend memory operation latency and improve the performance, our first key idea is to execute sub-operations in parallel.

## Slide 17: KEY IDEA I: PARALLELIZATION
There are two types of dependencies:
Deduplication
Integrity
Verification
Counter-mode Encryption
Inter-operation dependency
Intra-operation dependency
2. Dependency across different operations when they cooperate
1. Dependency within each operation
Notes: If we integrate different operations, we can see there is another type of dependency across different operations. We refer to them as the inter-operation dependency.

## Slide 18: KEY IDEA I: PARALLELIZATION
There are two types of dependencies:
Deduplication
Integrity
Verification
Counter-mode Encryption
Inter-operation dependency
Intra-operation dependency
Parallelizable
Sub-operations without dependency can execute in parallel
Notes: Sub-operations that do not have dependency in between can thus execute in parallel.

## Slide 19: KEY IDEA I: PARALLELIZATION
There are two types of dependencies:
Deduplication
Integrity
Verification
Counter-mode Encryption
Inter-operation dependency
Intra-operation dependency
Parallelizable
Sub-operations without dependency can execute in parallel

## Slide 20: KEY IDEA II: PRE-EXECUTION
Deduplication
Integrity
Verification
Counter-mode Encryption
Address
Data
A write consists of:
Sub-operations can pre-execute
as soon as their data/address dependency is resolved
External dependency
Notes: Second, we identify that a write consists of two parts: address and data.
Address and data also have dependency to the backend memory operations, which we refer to as the external dependency.
Sub-operations can pre-execute as soon as their data or address dependency is resolved

## Slide 21: KEY IDEA II: PRE-EXECUTION
Deduplication
Integrity
Verification
Counter-mode Encryption
Address
Data
A write consists of:
Address-dependent
Address-dependent sub-operations can pre-execute as soon as
the address of the write is available
Notes: We categorize sub-operations according to their external dependency.
The first category is address-dependent sub-operations that can pre-execute as soon as the address is available.

## Slide 22: KEY IDEA II: PRE-EXECUTION
Deduplication
Integrity
Verification
Counter-mode Encryption
Address
Data
A write consists of:
Data-dependent
Data-dependent sub-operations can pre-execute as soon as
the data of the write is available
Notes: The second category is data-dependent sub-operations that can pre-execute as soon as the data is available.

## Slide 23: KEY IDEA II: PRE-EXECUTION
Deduplication
Integrity
Verification
Counter-mode Encryption
Address
Data
A write consists of:
Both-dependent
Both-dependent sub-operations can pre-execute as soon as
both the data and address of the write are available
Notes: And the remaining sub-operations depend on both address and data. They can pre-execute when both address and data of the write are available.

## Slide 24: KEY IDEA II: PRE-EXECUTION
Deduplication
Integrity
Verification
Counter-mode Encryption
Address
Data
A write consists of:
How can we know the address/data ahead of time?
Notes: Second, we identify that a write consists of two parts: address and data.
Address and data also have dependency to the backend memory operations, which we refer to as the external dependency.
Sub-operations can pre-execute as soon as their data or address dependency is resolved

## Slide 25: AVAILABILITY OF ADDRESS AND DATA
Update tree node <Key, Value> using undo log
Backup
Location is known after traversal
During backup: Data of the update is known
Traverse tree with Key
Data for update
During backup: Address of the update is known
Pre-execution for update
Backup
Update
Commit
Use Pre-execution
Results
Pre-execution of address and data-dependent sub-operations
Take pre-executed results when writing back update
Notes: Let’s apply undo logging to tree node update.
This example shows how we can update the key with the new value.
First, it traverses the update location with key.
During the backup step, it makes a copy of the old data
During the update step, it performs in-place update.
Finally, in the commit step, it invalidates the backup copy and completes the transaction.
In this example, before the backup step, data is already known.
After tree traversal, the address is known.
Therefore, the pre-execution for update step can overlap with the backup step.
In the update step, it can take the pre-executed result to reduce the writeback latency.

## Slide 26: OUR PROPOSAL: JANUS
Janus is a Roman god with two faces:
When dependent data and address become available
Future
Past
Pre-execute operations with dependency resolved
one looks into the past
, and another into the future
Notes: To this end, we propose Janus.
The name Janus is a roman god with two faces.
One looking into the past and another into the future.
The past is the knowledge about when data and address become available.
And the future is we can pre-execute these operations before the write actually happens.

## Slide 27: JANUS OVERVIEW
Janus:
Serialized
Backup
Update
Commit
Parallelized
Parallelization
Parallelization reduces the latency of each operation
Timeline
Backup
Update
Commit
Backend memory operations
Original writeback latency
Notes: Based on our key ideas, we propose Janus.
The parallelization approach reduces the latency of each operation.

## Slide 28: JANUS OVERVIEW
Janus:
Serialized
Backup
Update
Commit
Parallelized
Pre-executed
Parallelization
Pre-execution
Pre-execution moves their latency off the critical path
Timeline
Backup
Update
Commit
Backup
Update
Commit
Commit
Update
Backend memory operations
Original writeback latency
Notes: And pre-execution further moves their latency off the critical path.

## Slide 29
Janus SW Interface
NVM Program
SW
HW
Janus HW
Memory
Controller
Core
Janus software interface enables pre-execution
Parallelization
Pre-execution
JANUS OVERVIEW
CPU
Notes: Here I am showing the overview of Janus. The Janus hardware is inside the memory controller. Janus integrates the two aforementioned key ideas: parallelization and pre-execution.
To enable pre-execution, Janus provides a software interface.
Next, I am showing the software interface.

## Slide 30: OUTLINE
BACKGROUND AND MOTIVATION
KEY IDEAS
JANUS MECHANISM
EVALUATION
CONCLUSION

## Slide 31: SOFTWARE INTERFACE
Janus provides functions for pre-executing address-, data-, and both-dependent sub-operations at object granularity
Janus interface is hardware-independent: only takes address and data
void updateTree(int key, item_t val) {
// find tree node with key
node* location = find(key);
// add old val to undo log
undo_log(location);
// update val
location->val = val;
persist_barrier();
// commit updates
commit();
}
1
2
3
4
5
6
7
8
9
10
11
The data for update is known
The address for update is known
Backup
Update
Commit
val
location
Notes: Janus provides functions for pre-execution for address, data, and both-dependent sub-operations.
The pre-execution operates at object granularity for best programmability.
The interface is hardware independent as it only takes the address and data of a write
Here I am showing the pseudo code of the previous undo logging example.
It has three steps: backup, update and commit
Before the backup step, we observe that the data for update is already know as shown in the function arguments.
The location for update is also known after traversing the tree.

## Slide 32: SOFTWARE INTERFACE
Janus provides functions for pre-executing address-, data-, and both-dependent sub-operations at object granularity
Janus interface is hardware-independent: only takes address and data
void updateTree(int key, item_t val) {
pre_t pre_obj; PRE_DATA(&pre_obj, &val, sizeof(item_t));
// find tree node with key
node* location = find(key);
PRE_ADDR(&pre_obj, location, sizeof(item_t));
// add old val to undo log
undo_log(location);
// update val
location->val = val;
persist_barrier();
// commit updates
commit();
}
1
2
3
4
5
6
7
8
9
10
11
12
13
PRE_ID
Thread_ID
Transaction_ID
Address
Size
Keep track of pre-execution:
Pre-execute data-dependent sub-operations
Pre-execute address-dependent sub-operations
Notes: Next, I am showing how to instrument the code with Janus interface.
First, we create a pre-execution object that keeps track of pre-execution.
Then, we place a function for pre-execution on data-dependent sub-operations, and a function for pre-execution on address dependent operations.

## Slide 33: AUTOMATED INSTURMENTATION
Manual instrumentation is effective at improving performance, but requires significant programmer’s effort
Janus provides a compiler pass to automatically instrument program with the interface
Compiler Pass
NVM Program
Dependency
Analysis
Data
Address
Instrumentation of Janus Interface
Notes: The previous example is done by programmers. It is effective, while requires significant programmer’s effort.
To minimize programmer effort, we provide a compiler pass to automate this process.
The workflow is the following:
The source code of the program is fed into Janus compiler pass. By dependency analysis on data and address, the pass instruments the interface functions.

## Slide 34
Janus SW Interface
NVM Program
SW
HW
Janus HW
Memory
Controller
Core
JANUS OVERVIEW
CPU
Parallelization
Pre-execution
Notes: Next, I will show the hardware of Janus in detail.

## Slide 35: HARDWARE MECHANISM
Memory Controller
Converter: convert pre-execution from object to cache line granularity
Intermediate result buffer: store pre-execution results to avoid changing processor/memory state
Correctness check: invalidate incorrect pre-execution
Backend memory operations
Core
Convert
Object
granularity
Cache line
granularity
Results
Intermediate Result Buffer
Object
granularity
Cache line
granularity
Backend memory operations
Intermediate Result Buffer
correctness check
Notes: The pre-execution request is send to a queue of object granularity. Then the converter converts the request into cache line granularity.
The converted request gets executed by backend memory operation logic as show in the figure.
To make sure pre-execution results does not change processor or memory state, Janus stores the results in the intermediate result buffer.
When the write arrives, Janus checks the correctness of pre-execution results before writing back to NVM.

## Slide 36: HARDWARE MECHANISM
Memory Controller
Backend memory operations
Core
Object
granularity
Cache line
granularity
Results
Intermediate Result Buffer
correctness check
PRE_BOTH X
Convert
Backend memory operations
Intermediate Result Buffer
Object
granularity
Cache line
granularity
X
X1
X2
WRITE X1
Take results
Write completes
Converter: convert pre-execution from object to cache line granularity
Intermediate result buffer: store pre-execution results to avoid changing processor/memory state
Correctness check: invalidate incorrect pre-execution
X1
X2
R1
R2
Notes: Next, I am showing the workflow.
Say there is a pre-execution request to location X.
First, it gets converted from object granularity to cache line granularity: X1 and X2.
Then, it is executed by the backend memory operation unit. The results are stored in the intermediate result buffer.
When the write arrives, it takes the corresponding result R1. After checking its correctness, Janus writeback the pre-executed result to NVM.
The correctness checking mechanism makes sure that incorrect pre-execution never cause correctness issue.

## Slide 37: OUTLINE
BACKGROUND AND MOTIVATION
KEY IDEAS
JANUS MECHANISM
EVALUATION
CONCLUSION

## Slide 38: METHODOLOGY
Gem5 Simulator:
Design points:
  Serialized: all backend memory operations are serialized
  Janus: pre-execute parallelized backend memory operations
Instrumentation of Janus functions:
Processor | Out-of-Order, 4GHz
L1 D/I, L2 cache | 64/32KB, 2MB per core (shared)
Backend memory operation cache | 512KB per core for each operation (shared)
Backend memory operation units | 4 units per core
Intermediate result buffer | 64 entries per core (shared)
Manual
Automated

## Slide 39: JANUS VS. BASELINE
Chart: Speedup over Serialized Baseline
| Array Swap | Queue | Hash | B-Tree | RB-Tree | TATP | TPCC | Geo. Mean
Parallelization | 1.334 | 1.3027 | 1.0714 | 1.6163 | 1.3302 | 1.4842 | 1.509 | 1.3433
Pre-execution | 0.68269 | 0.55897 | 0.11152 | 4.0543 | 0.43324 | 1.1959 | 2.2629 | 1.0098
Janus provides 2.35X speedup on average
2.35X Speedup

## Slide 40: JANUS VS. BASELINE
Chart: Speedup over Serialized Baseline
| Array Swap | Queue | Hash | B-Tree | RB-Tree | TATP | TPCC | Geo. Mean
Parallelization | 1.334 | 1.3027 | 1.0714 | 1.6163 | 1.3302 | 1.4842 | 1.509 | 1.3433
Pre-execution | 0.68269 | 0.55897 | 0.11152 | 4.0543 | 0.43324 | 1.1959 | 2.2629 | 1.0098
Pre-execution provides more speedup
Reduces the latency
Moves the latency off critical path

## Slide 41: MANUAL VS. AUTO INSTRUMENTATION
Chart: Speedup over Serialized Baseline
| Array Swap | Queue | Hash Table | B-Tree | RB-Tree | TATP | TPCC | Geo. Mean
Janus (Manual) | 2.0167 | 1.6561 | 1.1829 | 5.6706 | 1.7634 | 2.6801 | 3.7718 | 2.353
Janus (Auto) | 1.7754 | 1.1907 | 1.1103 | 5.2257 | 1.1502 | 2.4775 | 4.1924 | 2.039
Compiler pass provides close-to-manual performance
15% slower

## Slide 42: CONCLUSION
Problem
Storage and memory support for NVM systems increases write latency, which is on the critical path of NVM programs
Key Ideas
We observe that these operations can be divided into smaller sub-operations
We propose Janus, a software-hardware co-design that
  Parallelizes sub-operations if they are independent
  Pre-executes sub-operations if their dependencies are resolved
Results
Janus provides 2.35x speedup compared to serializing all operations
Janus provides a compiler pass for automated instrumentation

## Slide 43: Janus Optimizing Memory and Storage Support for Non-Volatile Memory Systems
Sihang Liu
Korakit Seemakhupt, Gennady Pekhimenko, Aasheesh Kolli, and Samira Khan

## Slide 44: BACKUP SLIDES

## Slide 45: SW INTERFACE
PRE_ADDR() | Pre-execute address-dependent sub-operations
PRE_DATA() | Pre-execute data-dependent sub-operations
PRE_BOTH() | Pre-execute all sub-operations
Pre-execution object (pre_obj):
Pre-execution functions:
PRE_ID | ID of the pre-executed NVM object
Thread_ID | ID of the current thread
Transaction_ID | ID of the current transaction
Address | Address of NVM object
Size | Size of NVM object
Match pre-execution with the actual write
Depending on the availability of address/data

## Slide 46: JANUS CORRECTNESS
Pre-execution requests can be incorrect
  Pre-executing wrong address or data
  Redundant pre-execution, etc.
Janus hardware always guarantees correctness
  The intermediate result buffer keeps a copy of the pre-executed data, and compare when the write takes the result
  Unused results are discarded after timeout
All correctness issues in using the interface only results in performance degradation

## Slide 47: WORKLOADS
Array Sway | Swap random items in an array
Queue | Randomly enqueue or dequeue queue nodes
Hash Table | Insert random values to a hash table
RB-Tree | Insert random values to a red-black tree
B-Tree | Insert random values to a b-tree
TATP | Update random records in the TATP benchmark
TPCC | Add new orders from the TPCC benchmark
Notes: Move to backup slides

## Slide 48: MULTICORE
Chart: Number of cores
| 1 | 2 | 4 | 8
 | 2.353 | 2.1889 | 2.0676 | 1.8674
Speedup decreases as the number of cores increases
Memory bandwidth becomes the bottleneck

## Slide 49: PRE-EXECUTION PERCENTAGE
Chart: Percentage over Total Operations
| Array Swap | Queue | Hash Table | B-Tree | RB-Tree | TATP | TPCC
Complete | 0.5 | 0.20574 | 0.47205 | 0.83061 | 0.28248 | 0.42859 | 0.78074
Incomplete | 0.16666 | 0.43389 | 0 | 0.04481 | 0.1948 | 0.28571 | 0

## Slide 50: JANUS VS. IDEAL
Chart: Slowdown over Non-blocking Witeback
| Array Swap | Queue | Hash | B-Tree | RB-Tree | TATP | TPCC | Geo. Mean
Serialized | 4.0042 | 2.7074 | 1.3181 | 11.4555 | 4.3416 | 13.7851 | 7.1822 | 4.9258
Janus | 1.9855 | 1.6348 | 1.1142 | 2.0202 | 2.462 | 5.1435 | 1.9042 | 2.0934
Compare Janus with the ideal case that has non-blocking writeback