## Slide 1: Crash Consistency in Encrypted Non-Volatile Main Memory Systems
Sihang Liu, Aasheesh Kolli, Jinglei Ren, and Samira Khan
Notes: Collaborated work between …

## Slide 2: NON-VOLATILE MAIN MEMORY BACKGROUND
Non-volatile DIMM
Non-Volatile Memories
High speed
Durable
Byte-addressable
System Requirement I
Crash consistency of NVMM programs
System Requirement II
Security guarantee by encryption

## Slide 3: REQUIREMENT I CRASH CONSISTENCY
Create Node
Head
Create Node
Switch Head
Fail to Recover
Head
Flush to NVMM
Switch Head
Crash Consistent
In Cache
In NVMM
[Intel PMDK, Coburn ’11, Volos1 ’11, Ren ’15, etc.]
Add a new node to a persistent linked list
Recent works provide high-level libraries
to provide crash consistency
Notes: First, let’s take a look at the crash consistency requirement
The figure shows a persistent linked list on NVMM. The head pointer points to the first node. In the process of appending a new node to the head, the new node first gets created in NVM. Then the head pointer switches this newly created node. However, if failure happens before the new node has reached NVM but after the head pointer in NVM gets updated. The whole linked list will fail to recover as the head node is missing.
To solve this problem, the program needs to flush the new node before switching the head pointer. In this way, even if there is a failure, program still recover. So it is crash consistent.
Recent works provide high-level libraries to provide crash consistency. Using these libraries, programmers do not need to manage such low-level p

## Slide 4: REQUIREMENT II NVMM ENCRYPTION
NVMM
username: admin
password: pwd
Durable
Security Problem!
Encryption
Attacker
Notes: As NVM is durable using crash consistency mechanisms, data on NVM is durable. However, an attacker with physical access to the NVM device can steal important data stored on the memory. So there is a security problem. To secure the data, the second requirement is encryption.

## Slide 5: OVERVIEW
Inconsistent
This work shows that crash consistency is
not guaranteed in encrypted NVMM systems
Consistent
Low-overhead
Our goal is to provide crash consistency
in encrypted NVMM systems
with low overhead
Notes: Here is an overview of this work.
We first show that current crash consistency mechanisms will fail on encrypted NVMM systems.
Our goal is to provide crash consistency support in encrypted NVMM systems with low overhead.

## Slide 6: NON-VOLATILE MEMORY ENCRYPTION NAIVE SOLUTION
Encrypt and decrypt data directly with the key
Read Access
Decryption
Time
Plaintext
Timeline for decryption
Every read access incurs
extra latency for decryption
To avoid extra latency, current works use counter-mode encryption
[Diffie and Hellman, 79]

## Slide 7
Instead of directly encrypting data,
counter-mode encryption
encrypts an unique counter for each cache line
Counter
Cache
Encryption Engine
Encrypted Memory
XOR
Processor
LLC
Counter
Encrypted Bitstring
Encrypt data with an unique counter
Encryption Engine generates
an Encrypted Bitstring
Writeback data XOR with
Encrypted Bitstring
Plaintext
Encrypted
Data
Generates Encrypted Data and
writes back to memory
Use an on-chip Counter Cache
for better performance
NON-VOLATILE MEMORY ENCRYPTION CURRENT COUNTER-MODE ENCRYPTION
[Yan ’06, Young ’15, Awad ’16]

## Slide 8: COUNTER-MODE ENCRYPTION READ ACCESS
Parallelized Read Access and Decryption
Read Access
Decryption
Time
Shorter Latency
Plaintext
From
Counter Cache
Notes: For a read access, the encryption step is now processed in parallel with the read access as the cached counter starts the decryption without data.

## Slide 9: COUNTER-MODE ENCRYPTION WRITE ACCESS
Encrypted NVMM
Each write access consists of
a data write and a counter write
Data
Counter
Notes: The write access first encryption data and then write data back. As the encrypted data needs its counter for correct decryption, each write access has a data write and a counter write.

## Slide 10: PROBLEM INCONSISTENT CONDITIONS
Data and counter NOT reaching NVMM
at the same time can cause inconsistency
Encrypted NVMM
Data
Counter
Inconsistent!
Notes: However, a failure happens when data has reached NVM while counter has not, or the counter has reached NVM while data has not, data and the counter are inconsistent. In both cases, decryption is unsuccessful.

## Slide 11
PROBLEM
Program can fail to recover if extending current crash consistency mechanism to encrypted NVMM
GOAL
Extend crash consistency mechanism to encrypted NVMM to provide a practical NVMM system

## Slide 12: REQUIREMENT CRASH CONSISTENCY IN ENCRYPTED NVMM
Data and counter reaching NVMM
at the same time ensures consistency
Encrypted NVMM
Data
Counter
Consistent
Notes: To make sure data and counter are always consistent even in event of a failure, data and counter have to reach NVM at the same time.

## Slide 13
COUNTER-ATOMICITY
Ensure data and the associated counter
reach NVMM atomically
KEY OBSERVATION
SELECTIVE COUNTER ATOMICITY
EVALUATION
PROBLEM
GOAL

## Slide 14
Counter-atomicity:
Requires data and the associated counter of
a write access reach NVMM atomically
Counter-atomic Write:
Write that satisfies counter-atomicity
Notes: Hereby, we propose counter-atomicity that requires data and counter reach NVM atomically. We refer to the writes that satisfies counter-atomicity as counter-atomic writes

## Slide 15
Challenge I:
How to ensure data and counter reach NVMM at the same time?
Notes: The first challenge is how to ensure the requirement of counter-atomicity?

## Slide 16: NAIVE SOLUTION CO-LOCATE DATA AND COUNTER IN ONE CACHE LINE
Counter-atomicity guaranteed: Data and counter always reach NVMM atomically
Co-located Data and its counter in a 72B cache line
Extend memory bus to 72bit
Encrypted NVMM
Processor
LLC
Counter Cache
However, it is costly to change the memory interface
72bit
Notes: The naïve solution is to collocate data and counter in the same cache line. So they can always be written back at the same time.
Counter-atomicity is guaranteed in this way.
However, this requires wider memory bus, requiring significant changes to the memory interface. It is expensive to add extra pins for a wider bus.

## Slide 17
Challenge II:
How to enforce counter-atomicity using the existing memory interface?

## Slide 18: IMPROVED SOLUTION USING EXISTING MEMORY INTERFACE
Write data and counter separately
Using the existing 64bit bus
Memory controller tracks the completion of data and counter writes, and blocks dependent writes
Encrypted NVMM
Processor
LLC
Counter Cache
64bit
Extra counter writes and blocking
Notes: To provide counter-atomicity using the same memory interface, we provide an improved solution. In this solution, data and counter are written back separately. To guarantee counter-atomicity, the memory controller tracks the completion status of data and counter – only when both of them have reached NVM, the write is complete. Dependent writes are blocked if the write is incomplete. So this solution ensures counter-atomicity using the existing memory bus. However, as data and counter are written back separately, this solution incurs additional counter write and blocking.

## Slide 19: DISADVANTAGE EXTRA COUNTER WRITEBACK
Write data
Encryption
Time
Write counter
Maintain existing memory system
But incurs 2X writes for data and counter
Write Access:
Notes: This time line shows the write access. As I have mentioned earlier, data and counter are written back separately, a counter-atomic write requires 2X writes.

## Slide 20: DISADVANTAGE BLOCKING DUE TO COUNTER-ATOMICITY
1
1
2
2
3
3
1
1
2
2
3
3
Time
Wait
Wait
Counter-Atomicity
(Worst Case)
No Counter-Atomicity
Data Write
Counter Write
Allows reordering, coalescing and buffering
Serialize writes in the worst case
TIME SAVED
Notes: The second disadvantage is blocking of dependent writes. This time line shows three dependent writes. Write 2 has to wait on the first write, and the third write has to wait for the second one. Whereas in the case without counter-atomicity, writes have the freedom for buffering, caching and coalescing. This solution can serialize the writes in the worst case.

## Slide 21: OVERHEAD FROM COUNTER-ATOMICITY
Incurs 2X write traffic due to counter write back
Incomplete write access blocks dependent writes
We refer to the design that enforce all writes
counter-atomic as full counter-atomicity
Notes: Let’s conclude the disadvantages. First, it requires twice number of writes. Second incomplete counter-atomic write blocks dependent writes. We refer to the solution where all writes are counter-atomic as full counter-atomicity.

## Slide 22
Is there any way to reduce
counter-atomicity overhead ?
Notes: So is there any way to reduce this overhead?

## Slide 23
COUNTER-ATOMICITY
KEY OBSERVATION
Not all writes need to be counter-atomic
SELECTIVE COUNTER ATOMICITY
EVALUATION
PROBLEM
GOAL
Notes: Our key observation for reducing this overhead is not all writes need to be counter-atomic.

## Slide 24: TRANSACTIONS FOR NVMM
Redo/Undo Logging
Journaling
Copy-on-Write, etc.
Maintain multiple copies of data for crash consistency
Only modify one copy at a time, and another one is valid
If system fails, recover from the valid copy
TANSACTIONS
CHARACTERISTICS
Original
Backup
Recover:
Backup consistent
Original data consistent
Backup
Original
Notes: Let me first briefly introduce crash consistency mechanisms. Typically, crash consistency mechanism use logging, journaling or copy-on-write mechanism. These mechanisms have the following characteristics. There are multiple copies of data for crash consistency, like this example, before modification, the program creates a backup copy. During medication, only one of the copies gets updated. If the system fails, it can either recover from the original data or the backup copy.

## Slide 25: EXAMPLE AN UNDO-LOGGING TRANSACTION
[Coburn ’13, Wang ’14, Kolli ’16, Nalli ’17, Joshi ’17, Hu ’17, etc.]
Undo Log
Original Data Structure
A
B
C
D
E
F
B
Prepare: Create the log entry and backup data
Mutate: Modify data structure in-place
Commit: Invalidate undo log entry
A
B
C
D
E
F
K
Update
CONSISTENT
INCONSISTENT
CONSISTENT
INCONSISTENT
INCONSISTENT
INCONSISTENT
Prepare
Mutate
Commit
persist_barrier
Prepare
Mutate
Commit
Notes: Let’s take a look at this example of an undo-logging transaction.
This example updates item B.
This transaction can be divided into three steps.
First, the program creates a backup copy and append it to the undo log in the prepare step. In this step, the original data is consistent as the backup is being created.
Then, it updates B to K in-place. Here, the backup serves as the consistent copy. We call this step mutate.
Finally, after update completes, it commits the original data structure and invalidates the backup. In this step, since the consistency status of original data and copy are changed at the same time, none of them is consistent.

## Slide 26: CONSISTENCY STATE IN TRANSACTION
 | Backup | Data | 
Prepare |  |  | 
Mutate |  |  | 
Commit |  |  | 
STAGES
CONSISTENT?
Need
Counter-Atomicity?
Only COMMIT needs to be counter-atomic
Key Insight:
Writes that do not immediately affect crash consistency do not need counter-atomicity
Notes: We can conclude that, in the prepare step, original data is consistent. In the mutate step, backup is consistent. Finally in the commit step, none of them is consistent. Therefore, the first to steps do not reply on counter-atomicity to ensure crash consistency. While in the last commit step, counter-atomicty is necessary as there is no consistent copy.

## Slide 27
COUNTER-ATOMICITY
KEY OBSERVATION
SELECTIVE COUNTER ATOMICITY
Enforce counter-atomicity only for the writes that immediately affect the consistency state
EVALUATION
PROBLEM
GOAL
Notes: According to this observation, we propose selective counter-atomicity that only enforce counter-atomicity for the writes that immediately affect the consistency state.

## Slide 28: SOFTWARE SUPPORT FOR SELECTIVE COUNTER-ATOMICITY
Annotation for
Selective Counter-Atomicity
Compile
NVMM
Program
Annotated
Code
Source Code
SW
Notes: To support selective counter-atomicity, we first provide this SW support. The NVMM program first gets annotated to support selective counter-atomicity, then gets compiled into executable.
We propose two low-level primitives for annotation.

## Slide 29: PRIMITIVES APPLYING SELECTIVE COUTNER-ATOMICITY
CounterAtomic Variables
Any variable that directly affects the consistency state needs to be counter-atomic
counter_cache_writeback() Function
Write back a cache line of counter for the specified location to NVMM, similar to data cache writeback
Notes: First, programmer needs to annotate variables that directly affects the crash consistency, like the previous commit operation as CounterAtomic.
Second, to writeback newly updated counters from cache to NVMM, we propose counter_cache_writeback. This is similar to data cache writeback operation, such as clwb.

## Slide 30: EXAMPLE APPLYING PRIMITIVES
Prepare
Mutate
Commit
counter_cache_writeback
data logs
counter_cache_writeback
in-place updates
Update validity counter-atomically
persist_barrier
Notes: Here is an example for applying these primitives. After the prepare step, the program writes back counters before the persist_barrier. Similarly, after mutate, counters also need to be written back. In the final commit step, the valid bit for backup is counter-atomically updated. So in this example, only the update to the valid bit needs to be counter-atomic.

## Slide 31: HARDWARE SUPPORT FOR SELECTIVE COUNTER-ATOMICITY
Memory Controller
Processor
Encrypted NVMM
Read/Write
Counter-Atomic?
Data/Counter
64bit
HW
Annotation:
CounterAtomic
counter_cache_writeback()
Compile
NVMM
Program
Annotated
Code
Source Code
SW
Notes: Next comes the HW support. The annotated program feeds into the processor. The memory controller performs counter-atomic writs for the annotated ones. Data or counter gets persisted into NVMM through the 64bit bus.
Let’s take a closer look at the memory controller.

## Slide 32: HARDWARE IMPLEMENTATION MEMORY CONTROLLER
Counter
Cache
Encryption Engine
NVM
Coordinator
Counter
Write Queue
Data
Write Queue
Processor
LLC
Cache counters for fast decryption
Control writes to NVMM
Encrypt/Decrypt data with counters
Battery
Protected by residual battery
Counter
Cache
Encryption Engine
NVM
Coordinator
ENCRYPTED DATA
COUNTERS
Encrypted NVMM
Write Queues keep track of counter-atomic data and counter writes
[e.g., Intel ADR]

## Slide 33: HARDWARE IMPLEMENTATION DETAILS ABOUT WRITE QUEUES
Encrypted NVMM
Counter
Write Queue
Data
Write Queue
WRITE 0x100
Data 0x100
Counter 0x100
0
Ready Bit
Ready Bit
Ready Bit is set only if both data and counter writes have reached their write queues
Ready
1
1
Battery
FAILURE
Only flush READY entries:
Ensure counter-atomicity
Ready
NOT Ready
[Intel ADR]
Notes: The key of this design is the write queues. This example shows a writeback of counter-atomic data in address 0x100. First the data reaches the persistent data write queue. The ready bit is 0 as counter is not available. Then counter for 0x100 arrives. Ready bit for both entries get updated at the same time. Note that the set operation is covered by battery. If failure happens, the battery-backed write queues only writeback ready entries.
We can use Gang set/clear both ready bits.

## Slide 34
COUNTER-ATOMICITY
KEY OBSERVATION
SELECTIVE COUNTER ATOMICITY
EVALUATION
PROBLEM
GOAL

## Slide 35: EVALUATION SIMULATED SYSTEM
Processor | x86 Out-of-Order (Gem5)
L1 D/I Cache | 64/32KB (private)
L2 Cache | 2MB per core (shared)
Counter Cache | 1MB per core (shared)
Memory | 8GB PCM
Encryption Latency | 40ns
Notes: This is the gem5-based simulation configuration.

## Slide 36: EVALUATION DESIGN POINTS
DESIGN DESCRIPTION | SHORTHAND
No-encryption design | NoEncryption
Ideal design w/o counter-atomicity overhead | Ideal
Co-located data and counter using a wider bus | ExtendedBus
Full counter-atomicity | FCA
Selective counter-atomicity | SCA
Notes: We have the following design points for comparison.
line by line

## Slide 37: EVALUATION BENCHMARK SUITE
Array Swap
Queue
Hash Table
B-Tree
RB-Tree

## Slide 38: EVALUATION MULTICORE (EIGHT) THROUGHPUT
Number of transaction per second (transaction size 64B)
Chart: Avg. Throughput Norm. to Single-Core NoEncryption
| SCA | FCA | ExtendedBus
8 Core | 2.9821 | 2.1248 | 3.3012
Selective vs. Full Counter-Atomicity
40% faster
Selective Counter-Atomicity vs. ExtendedBus
Within 10% slowdown
Wider memory bus (72bit vs. 64bit)
10% Slower
40% Faster
Notes: In a 8-core system, SCA is 40% than FCA. Compared to the extended bus solution, SCA is within 10% slowdown. Note that the extended bus solution is impractical.

## Slide 39: EVALUATION VARIABLE TRANSACTION SIZE
Chart: Number of 64B Cache Lines
| 1 | 2 | 4 | 8 | 16 | 32 | 64
 | 1.0747 | 1.0523 | 1.0386 | 1.0223 | 1.0124 | 1.0064 | 1.0034
7.7%
< 1%
Selective counter-atomicity has negligible overhead if manipulating large dataset during transaction
As transaction size increase, overhead of SCA decrease
Notes: Next, we evaluate the overhead from SCA. Compared to the ideal case that does not have any counter-atomicity overhead, the overhead from counter-atomicity is 7.7% in 64B transactions. As the transaction size increase, the overhead can be lower than 1%. We conclude that SCA has negligible overhead if manipulating large datasets, which commonly appear in real-world applications.

## Slide 40: SUMMARY
Existing crash consistency mechanisms do not extend to encrypted NVMM systems
Counter-atomicity: data and its counter writes are atomic
Selective counter-atomicity: reduces atomicity overhead
Track data and its counter write in the memory controller,
and maintain existing memory interface
Selective vs. Full Counter-Atomicity: 40% faster
Selective vs. Ideal Design: < 7.7% overhead
PROBLEM
MECHANISM
RESULTS
CONTRIBUTION

## Slide 41: Crash Consistency in Encrypted Non-Volatile Main Memory Systems
Sihang Liu, Aasheesh Kolli, Jinglei Ren, and Samira Khan
Notes: Collaborated work between …

## Slide 42: BACKUP SLIDES

## Slide 43: EVALUATION THROUGHPUT
Chart: Throughput Norm. to Single-Core NoEncryption
| SCA | FCA | ExtendedBus
1 Core | 0.89863 | 0.84526 | 0.90428
2 Core | 1.4856 | 1.3325 | 1.5417
4 Core | 2.2832 | 1.8739 | 2.4442
8 Core | 2.9821 | 2.1248 | 3.3012
Number of transaction per second (transaction size 64B)
Notes: Show 8 core only
2 Conclusions in bottom
Within 10% instead of …

## Slide 44: EVALUATION VARIABLE COUNTER CACHE SIZE
Chart: Workload Footprint
| 100MB | 500MB | 1000MB
256KB | 1.0072 | 1.007 | 1.0063
512KB | 1.0153 | 1.0137 | 1.0127
1MB | 1.024 | 1.0187 | 1.018
2MB | 1.0335 | 1.0215 | 1.0199
4MB | 1.0516 | 1.0252 | 1.0215
8MB | 1.0902 | 1.0313 | 1.0242

## Slide 45: COMPARISON
 | Naive Solution | Improved Solution
Write Access | Data and Counter co-located (72B) | Data or Counter Separated (64B)
Memory Interface |  | 
Counter Cache Miss | Fetch only 1 counter (72B transfer) | Fetch 8 counters (64B transfer)
Extend to 72bit bus
Existing 64bit bus

## Slide 46: EXAMPLE USING SELECTIVE COUNTER-ATOMICITY PRIMITIVES
UndoTx (Backup* log, item_t* data) {
  PrepareLog(log, data); //prepare
  counter_cache_writeback(log);
  persist_barrier();
  MutateData(data); //mutate
  counter_cache_writeback(data);
  persist_barrier();
  log->valid = false; //commit
  persist_barrier();
}
struct Backup {
  item_t item;
  CounterAtomic bool; valid;
};
valid alters the consistent state of both log and original data structure
Write back the counters for the undo log entry
Write back the counters for the in-place data structure