## Slide 1: Write Prediction for Persistent Memory Systems
Suyash Mahar, Sihang Liu, Korakit Seemakhupt,
Vinson Young, Samira Khan
PACT 2021
Artifact Available: pmweaver.persistentmemory.org

## Slide 2: Summary
Motivation
Persistent memory (PM) is a non-volatile, byte-addressable memory
PM programs need explicit store ordering for recoverability
PM stores also need support for encryption, deduplication…
Ordering and PM-support operations leads to application slowdown
Solution: PMWeaver
Predicts PM stores and hides the extra latency using precomputation
PMWeaver: Software transparent PM write prediction
Performance
1.63x improvement in performance over baseline

## Slide 3: Background
PM Programming

## Slide 4: PM Progr. and Background
Intel DC-PMM
Persistent Memory allows:
  Byte addressability
  Small latency access
  Low cost per GiB
Persistent memory is non-volatile and crash-consistent
Commercially available as Intel Optane DC-PMM.
PM Programming
Crash-consistency requires explicit store ordering
Thus, updates to PM are required to be ordered and frequently flushed

## Slide 5: PM Prog. Example
Steps
Create a new node
Backup the old head
Update head
Invalidate the backup
void push_front_list(int val) {
auto *new_node = pmalloc(...);
new_node->data = val;
new_node->next = head;
backup = head;
backup_valid = 1;
persist_barrier();
head = new_node;
persist_barrier();
backup_valid = 0;
}
PM Programming requires frequent and ordered writebacks
Insert a new head node to a PM list

## Slide 6: PM Writeback Timeline
Lifecycle of a PM writeback:

## Slide 7: PM Writeback Timeline
Lifecycle of a PM writeback:
Volatile Domain
Persistent Domain
Core
Cache
Memory
Controller
PM
ST-A
ST-B
ST-C
PersistBarrier()
Instructions

## Slide 8: PM Write Latency
Each write to PM writeback requires:
Core
Cache
Memory
Controller
PM
Core
Cache
Memory
Controller
PM
Timeline
Execution
continues
Write
PersistBarrier()
Cache Writeback
Memory Controller
NVM Access

## Slide 9: PM Support Operations
Encryption, deduplication… add extra latency to a PM writeback
Core
Cache
Memory
Controller
PM
Timeline
Execution
continues
Write
PersistBarrier()
Cache Writeback
Memory Controller
NVM Access

## Slide 10: PM Support Operations
Encryption, deduplication… add extra latency to a PM writeback
Timeline
Cache Writeback
Memory Controller
NVM Access
Execution
continues
Write
PersistBarrier()
PM-Support Operations
Core
Cache
Memory
Controller
PM

## Slide 11: Precomputation
Precomputing PM-Support Operations moves latency off critical path
Timeline
Execution
continues
Write
PersistBarrier()
Core
Cache
Memory
Controller
PM

## Slide 12: Precomputation
Precomputing PM-Support Operations moves latency off critical path
Timeline
Execution
continues
Write
PersistBarrier()
Core
Cache
Memory
Controller
PM
Precompute Support Operations by predicting PM Writebacks

## Slide 13: Outline
Background and Motivation
Challenges and Observations
PMWeaver Mechanism
Evaluation
Conclusion

## Slide 14: Challenges - Overview
Core
PM
Challenge 1
Predicting PM Writebacks
Challenge 2
Triggering predictions
?
store 1
store 2
writeback
(addr, data)
writeback
?
prediction

## Slide 15: Challenge - I
How to predict a writeback to improve system performance?

## Slide 16: Observation
Stores prior to a writeback carry the writeback’s data and address
Example:
1 void update(entry_t *location, entry_t new_data) {
2
3 // 1. Prepare backup
4 ...
5
6 *location = new_data;
7 persist_barrier(...);
8
9 // 2. Invalidate backup
10 ...
11 }
Instr | Addr | Data
St-1 | ... | 
St-2 | ... | 
St-3 | 0x7f08 | 0xcafe
St-4 | ... | 
St-5 | 0x7f90 | 0xbaad
St-6 | ... | 
St-7 | ... | 
St-8 | 0xbaad | 0xcafe
CLWB |  | 
SFENCE |  | 
Instruction Trace
Store instructions predict future PM writebacks

## Slide 17: Challenges - Overview
Core
PM
Challenge 1
Predicting PM Writebacks
Challenge 2
Triggering predictions
?
store 1
store 2
writeback
(addr, data)
writeback
?
prediction

## Slide 18: Challenge - II
How to trigger a prediction?

## Slide 19: Challenge – Prediction Trigger
PM Transaction Example:
void listInsertHead(int new_data) {
TX_BEGIN {
auto *node = TX_NEW(node_t); // Allocate new node
// Init the new node
...
TX_ADD(head->next);
head->next = node;
TX_ADD(head); // Backup head
head = node;
} TX_END
}

## Slide 20: Challenge - Trigger
Naïve Solution: Trigger predictions with the first store.
Problem: Trigger instruction shared across different calls
void listInsertData(string new_data) {
string val = compute(new_data);
int len = len(new_data);
TX_BEGIN {
auto *node = TX_NEW(node_t);
...
} TX_END
}
void listInsertEmpty() {
TX_BEGIN {
auto *node = TX_NEW(node_t);
...
} TX_END
}
False trigger sharing

## Slide 21: Observation
Prediction are unique to their context
Using sequence of store PCs leading to the first contributing store
21
21
Use n store PCs leading to the first contributing store as trigger
void listInsertData(string new_data) {
string val = compute(new_data);
int len = len(new_data);
TX_BEGIN {
auto *node = TX_NEW(node_t);
...
} TX_END
}
void listInsertEmpty() {
TX_BEGIN {
auto *node = TX_NEW(node_t);
...
} TX_END
}
Unique Context
PC Path

## Slide 22: PMWeaver
Write Prediction for Persistent Memory

## Slide 23: Overview
1: Learner
PMWeaver works in three stages:
2: Predictor
3. Validator
Learn relation between store instructions and PM writebacks
Combine learned combination of store instructions to a writeback prediction
Resolve mispredictions on the arrival of the real writeback

## Slide 24: 1. Walkthrough - Learner
PC Addr Data
PC-1 A1 0xaaaa
PC-2 A2 0xbbbb
PC-3 A3 0x1000
PC-4 0x1000 0xbbbb
PC-5 0x1008 0xaaaa
...//writeback pc-4,5
St-6 0x7f18 0x5600
St-7 0x7f10 0x5608
St-8 0x7f28 0x5610
St-9 0x7f80 0x1080
St-10 0x7f88 0x1088
...//write-back st-9,10
Data PC PC-Path
Execution Trace
Store History Buffer
Φ
PC-Path Predictor Entry
0xaaaa PC-1 Φ
0xbbbb PC-2 ...
0x1000 PC-3 ...
0x1000 ⟵ 0xaaaabbbb
Writeback
Predictor Table
...
PC-1,
PC-2,
PC-3
Tracks recent store instructions
Tracks learned relationships
Record store instructions
Record store instructions
Find stores to predict data
Find stores to predict address
Add prediction relationship to the Predictor Table
addr
data
Context of the first store
Address
Data

## Slide 25: Overview
1: Learner
2: Predictor
3. Validator

## Slide 26: 2. Walkthrough - Predictor
0xaaaa PC-1 Φ
0xcccc
0xbbbb PC-2 ...
0x1000 PC-3 ...
... ... ...
Data PC PC-Path
Execution Trace
Store History Buffer
Φ PC-2, PC-1, PC-3
PC-Path Predictor Entry
Predictor Table
PC Addr Data
PC-1 A1 0xaaaa.
PC-2 A2 0xbbbb.
PC-3 A3 0x1000.
PC-4 0x1000 0xbbbb.
PC-5 0x1008 0xaaaa.
writeback pc-4,5
PC-1 A4 0xcccc
PC-2 A5 0xdddd
PC-3 A6 0x2000
PC-Path
Φ
Prediction Triggered
Prediction
Address Data
0xdddd,
0x2000
Wait for the trigger
PC-1’s context matches (PC-Path)
Prediction starts
Wait for stores to contribute to the prediction
Send prediction for validation
⊕
Calculate PC-1’s PC Path
Address
Data

## Slide 27: Overview
1: Learner
2: Predictor
3. Validator

## Slide 28: 3. Validator
PC Addr Data
PC-1 A1 0xaaaa.
PC-2 A2 0xbbbb
PC-3 A3 0x1000.
PC-4 0x1040 0xbbbb.
PC-5 0x1048 0xaaaa.
writeback pc-4,5
PC-1 A4 0xcccc.
PC-2 A5 0xdddd.
PC-3 A6 0x2000.
PC-4 0x1080 0xdddd.
PC-5 0x1088 0xcccc.
writeback pc-9,10
Execution Trace
0x2000 ⟵ 0xccccdddd
Writeback
0x1080 cccc dddd
PM Addr Prediction Data
Prediction Result Buffer
Compare
Update PM State
Compare writeback with prediction
addr
data
Address
Data

## Slide 29: 3. Validator
PC Addr Data
PC-1 A1 0xaaaa.
PC-2 A2 0xbbbb
PC-3 A3 0x1000.
PC-4 0x1040 0xbbbb.
PC-5 0x1048 0xaaaa.
writeback pc-4,5
PC-1 A4 0xcccc.
PC-2 A5 0xdddd.
PC-3 A6 0x2000.
PC-4 0x1080 0xdddd.
PC-5 0x1088 0xcccc.
writeback pc-9,10
Execution Trace
0x2000 ⟵ 0xccccdddd
Writeback
0x1080 cccc dddd
PM Addr Prediction Data
Prediction Result Buffer
Compare
Recalculate
PM-Support Operations
addr
data
Recalculate on misprediction
Address
Data

## Slide 30: Evaluation

## Slide 31: Methodology
Gem5 Simulator:
Processor Out-of-order, 3.0 GHz
L1 i/d 32KiB each
L2/L3 128KiB/2MB per core
PC-Path length 16
Workloads:
Low-level: Linked List, Hashmap, Array Swap, TATP, TPCC
Transaction: B-Tree, C-Tree, RB-Tree, Skiplist, Hashmap TX
PM-Support Operations:
Encryption and Integrity Verification (Encr+Veri)
Deduplication (Dedup)

## Slide 32: Performance Improvement
Chart: Execution Time Normalized to No PM-Support operation
| B-Tree | C-Tree | RB-Tree | Skiplist | Hashmap TX | Linked List | Hashmap Low-level | ArraySwap | TATP | TPCC | GMean
Enc+Veri | 1.8352 | 1.4119 | 1.7536 | 1.6038 | 1.6792 | 4.3259 | 6.013 | 6.6191 | 1.8395 | 4.2081 | 2.6378
Enc+Veri w/ PMWeaver | 1.3347 | 1.1015 | 1.2479 | 1.1845 | 1.2894 | 1.8859 | 3.963 | 2.9453 | 1.0038 | 2.4811 | 1.6544
Column1
Dedup | 1.4662 | 1.2301 | 1.421 | 1.3361 | 1.3777 | 2.8475 | 3.426 | 3.8985 | 1.4758 | 2.7377 | 1.9321
Dedup w/ PMWeaver | 1.2602 | 1.1034 | 1.2699 | 1.2007 | 1.2723 | 1.8779 | 3.2694 | 2.0785 | 1.0027 | 2.0379 | 1.5301
1.63x
1.26x
PMWeaver provides a significant performance improvement

## Slide 33: Prediction Coverage
Chart: Coverage (% writebacks)
| B-Tree | C-Tree | RB-Tree | Skiplist | Hashmap TX | Linked List | Hashmap Low-level | Array Swap | TATP | TPCC | AMean
Address Enc+Veri w/ PMWeaver | 73.6672 | 85.4031 | 86.4364 | 80.4197 | 79.5146 | 92.7365 | 47.3208 | 71.9286 | 99.6336 | 77.8293 | 79.489
Data Enc+Veri w/ PMWeaver | 39.6052 | 61.5174 | 30.7934 | 40.9114 | 27.1271 | 64.0203 | 9.325 | 67.4 | 99.4337 | 49.7644 | 48.9898
Address Coverage
Data Coverage
81%
50%
PMWeaver is effective in predicting majority of PM writebacks

## Slide 34: Conclusion
Problem
Hide PM-write and support operation latency in a S/W transparent manner
Key Idea
Predict PM writebacks and precompute their results ahead of time
We propose PMWeaver that predicts future PM writebacks using past stores
Results
PMWeaver provides: 1.63x speedup for Encryption and Integrity Verification 1.26x speedup for Deduplication
PMWeaver is software-transparent and requires no change to ISA/source code

## Slide 35: Write Prediction for Persistent Memory Systems
Suyash Mahar, Sihang Liu, Korakit Seemakhupt,
Vinson Young, Samira Khan
PACT 2021
Artifact Available: pmweaver.persistentmemory.org

## Slide 36
-

## Slide 37: Backup Slides

## Slide 38: PM Performance Overhead
Enforcing ordering of PM writes bring them to the critical path
Moreover, processing those PM writes will slowdown the application
  PM-Support Operations: Encryption, deduplication…
E.g., Encryption and Integrity verification results in 2.54x slowdown
Solution: Predict PM-writes and pre-compute PM-support operations
PMWeaver hides write latency by predicting PM writes

## Slide 39: PM Writeback Timeline
Lifecycle of a PM writeback:
Cache
ST-A
ST-B
ST-C
PersistBarrier()
Processor
Memory
Controller
PM
Volatile Domain
Persistent Domain
Instructions

## Slide 40: 1. Learner
The learner in PMWeaver performs two functions:
On a store,
  Add the store to a fixed length buffer, the Store History Buffer
On a writeback,
  Look the recent stores that can predict the address and data of the writeback.
  Send the learned relation between stores and writeback to the Predictor.
Learner: Identify relationship between stores and writebacks

## Slide 41: 2. Predictor
Predictor combines data from store instructions to predict a writeback
To trigger a prediction, the Predictor keeps track of the current PC-Path
Once triggered, the Predictor waits for all stores to contribute their data
Predictor: Looks out for trigger and combines store instructions to predict writebacks

## Slide 42: 2. Validator
Validator buffers the predictions and their computed metadata
When writeback arrives at the Validator, predicted writeback is verified.
If correct, the PM state is updated
Otherwise, the prediction is dropped
Validator: Resolves mispredictions using the real writeback

## Slide 43: Challenge - Trigger
PM Transaction Example:
void listInsertHead(int new_data) {
TX_BEGIN {
auto *node = TX_NEW(node_t); // Allocate new node
// Init the new node
TX_ADD(head->next);
head->next = node;
TX_ADD(head); // Backup head
head = node;
} TX_END
}
Instr | Addr | Data
St-1 | ... | 
St-2 | ... | 
St-3 | 0x7f08 | 0x1040
St-4 | ... | 
St-5 | 0x7f90 | 0xbbaa
St-6 | ... | 
St-7 | ... | 
St-8 | 0x1040 | 0xbbaa
CLWB |  | 
SFENCE |  | 

## Slide 44: Observation - Prediction
Need for PM writeback prediction
Naïve solution: Precompute PM-support operation from cache
Time between write to the cache and the writeback is too short
Core
Cache
Memory
Controller
PM
Core
Cache
Memory
Controller
PM
Write
PersistBarrier()
77%
PM Writeback needs to be predicted early enough to hide its latency

## Slide 45: 3. Validator
PC Addr Data
0x18 A1 0xcafe.
0x10 A2 0xf00d
0x28 A3 0x1040.
0x80 0x1040 0xf00d.
0x88 0x1048 0xcafe.
writeback st-4,5
0x18 A4 0xbeef.
0x10 A5 0xdead.
0x28 A6 0x1080.
0x7f80 0x1080 0xabcd.
0x7f88 0x1088 0x0200.
writeback st-9,10
Data PC PC-Path
Execution Trace
Store History Buffer
0x1234 0x7f10, 0x7f18, 0x7f28
PC-Path Predictor Entry
0xcafe 0x18 0x1234
0xf00d 0x10 0x760a
0x1040 0x7f28 0x442d
... ... ...
*0x1080 ⟵ 0xdeadbeef
Writeback
Predictor Table
0x1080 0xdead beef
PM Addr Prediction Data
PC-Path
0x1234
Prediction Result Buffer
Compare
Update PM State
Validate prediction

## Slide 46: Prior Work
Software based prediction (Janus):
Prior work uses software hints to precompute PM-Support Operations
Address and data of a future write-back is provided as a hint to the HW
Software based prediction is limited:
Requires changes to ISA and source code
Requires programmer to obtain address and data ahead of a write-back
Software hints result in overhead from additional function calls
Not possible to precompute across control flow edges (branches, loops)
Precomputing PM-Support Operation requires a software transparent solution

## Slide 47: PMWeaver vs Janus
TODO: Add plot

## Slide 48: Challenge - Trigger
Naïve Solution: Trigger predictions with the first contributing store.
Problem: Trigger instruction shared across different calls
void listInsertHead(int new_data) {
TX_BEGIN {
auto *node = TX_NEW(node_t); // Allocate new node
// Init the new node
TX_ADD(head->prev);
head->prev = node;
TX_ADD(head); // Backup head
head = node;
} TX_END
}
Instr | Addr | Data
St-1 | ... | 
St-2 | ... | 
St-3 | 0x7f08 | 0x1040
St-4 | ... | 
St-5 | 0x7f90 | 0xbbaa
St-6 | ... | 
St-7 | ... | 
St-8 | 0x1040 | 0xbbaa
CLWB |  | 
SFENCE |  | 

## Slide 49: Observation
Prediction are unique to a context
Using sequence of store PCs to the first store creates a unique context
49
49
void listInsertHead(int new_data) {
TX_BEGIN {
auto *node = TX_NEW(node_t); // Allocate new node
// Init the new node
TX_ADD(head->prev);
head->prev = node;
TX_ADD(head); // Backup head
head = node;
} TX_END
}
Instr | Addr | Data
St-1 | ... | 
St-2 | ... | 
St-3 | 0x7f08 | 0x1040
St-4 | ... | 
St-5 | 0x7f90 | 0xbbaa
St-6 | ... | 
St-7 | ... | 
St-8 | 0x1040 | 0xbbaa
CLWB |  | 
SFENCE |  | 
PC Path
Use store n PCs leading to the first store as the trigger

## Slide 50: Observation
Predictability of PM writebacks
PM writebacks are frequently predicted by previous stores
We studied stores and PM writebacks across ten PM workloads
Chart: % of Predictable Writebacks
| B-Tree | C-Tree | RB-Tree | Skiplist | Hashmap TX | Linked List | Hashmap Low-Level | Array Swap | TATP | TPCC | A-Mean
Addr | 51 | 65 | 72 | 71 | 67 | 99 | 100 | 100 | 100 | 85 | 81
80.7% of writebacks
are predictable
Store instructions often predict future PM writebacks

## Slide 51
⊕
Address
Data

## Slide 52: Observation
Chart: Top 20 Unique store PC sets
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Series 1 | 35.1861 | 9.2413 | 6.6658 | 3.6489 | 2.8904 | 2.4706 | 2.2115 | 2.0043 | 1.8853 | 1.5861 | 1.3308 | 1.1916 | 0.64644 | 0.62807 | 0.60431 | 0.5337 | 0.47076 | 0.45406 | 0.4369 | 0.4106
Reusability of the relationship between stores and PM writebacks
PM writebacks are predicted by the same set of stores repeatedly
20
Top 20 PC sets predict 74.5% of all PM Writebacks
Store instructions repeatedly predict future PM writebacks